## Slide 1: Learning a High-Precision Robotic Assembly Task Using Pose Estimation from Simulated Depth Images
Litvak, Y., Biess, A., & Bar-Hillel, A., 2019, International Conference of Robotics and Automation‏
Presented by: Guy Farjon, Amit Cohen, Nitzan Levy

## Slide 2: Today’s Talk
Introducing the Siemens Innovation Challenge
  Solving a generic assembly task
  Why is it hard?
Changing perspective – parts assembly as a pose estimation problem
  Coarse and refined pose estimation
  Bridging the simulation-reality gap
  Fusing components for task completion
Experiments and Results
Conclusions
Our thoughts

## Slide 3: The Task
Assembling of a gear-like mechanism
  A base, 3 gears, and 2 shafts
Previous work mainly focused on grasping the objects
  Grasping unknown objects
  Plan the motion towards the object
This work focuses on the full assembly task
  Perception as a main component
  Combine multiple HW and SW solutions
Bottom line – observe, detect, grasp, assemble
  An engineered solution to a complex task
ROS
Kuka LBR IIWA 14 R820
SAKE ROBOTICS EZGripper
Intel RealSense D415
SunRise
Gazebo
Moveit!
Python (TensorFlow)
OpenCV
…

## Slide 4: Method
1. Lin, T. Y., Goyal, P., Girshick, R., He, K., & Dollár, P. (2017). Focal loss for dense object detection. ICCV‏
Simulate the environment
  Create a huge datasets in seconds
  Train a pose estimation pipe on synthetic images (based on RetinaNet1)

## Slide 5: Method
1. Lin, T. Y., Goyal, P., Girshick, R., He, K., & Dollár, P. (2017). Focal loss for dense object detection. ICCV‏
before
after
Simulate the environment
  Create a huge datasets in seconds
  Train a pose estimation pipe on synthetic images (based on RetinaNet1)
Estimate the parts’ poses using RGB-D images
  Average 10-images to eliminate noise
  Bridge the simulation-reality gap
Sim.
Reality

## Slide 6: Method
1. Lin, T. Y., Goyal, P., Girshick, R., He, K., & Dollár, P. (2017). Focal loss for dense object detection. ICCV‏
Simulate the environment
  Create a huge datasets in seconds
  Train a pose estimation pipe on synthetic images (based on RetinaNet1)
Estimate the parts’ poses using RGB-D images
  Average 10-images to eliminate noise
  Bridge the simulation-reality gap
Calculate pick-and-place motions for each part
  Use prior knowledge to place the parts in the correct location
  ‘Moveit!’ for motion trajectory

## Slide 7: Method
Simulate the environment
  Create a huge datasets in seconds
  Train a pose estimation pipe on synthetic images (based on RetinaNet1)
Estimate the parts’ poses using RGB-D images
  Average 10-images to eliminate noise
  Bridge the simulation-reality gap
Calculate pick-and-place motions for each part
  Use prior knowledge to place the parts in the correct location
  ‘Moveit!’ for motion trajectory
Anything you can do, I can do better
  Manipulate the robot from the simulation
1. Lin, T. Y., Goyal, P., Girshick, R., He, K., & Dollár, P. (2017). Focal loss for dense object detection. ICCV‏

## Slide 8: Experiments and Results
58 assembly attempts with a success rate of 67.2%
Average results and standard deviations
https://www.youtube.com/watch?v=uMvq2-Tg-9g&t=62s

## Slide 9: Conclusion
Assembly tasks can be treated as a pose estimation problem
  With simulated components
  When 3D CAD files are available
  Using pre-defined conditions and configurations
The simulation-to-reality gap can be significantly bridged
  Using depth images and image processing tools
Don’t give up
  3 stages for extremely accurate pose estimation
  Stitching up a solution for each specific problem

## Slide 10: Our thoughts
Each subproblem was solved independently
  May result with difficulties when trying new assembly tasks
Only rigid objects were examined
The solution requires a CAD model
  Usually not accessible to the end user
  Utilize depth information (e.g., point cloud etc.) instead of prior knowledge
Grasping and placing of objects is pre-defined
  RL methods might reduce the high setup costs
  Does not include planning algorithms for optimized assembly
Overall – amazing solution of extremely complex assembly task